REDSKY CHECKLISTS
CHECKLISTS
This checklist is a guide to coordinate Pilot Operating Handbook
and STC data applicable to this particular aircraft only.
The applicable Pilot Operating Handbook and STC installations
 remain the official documentation for this aircraft.
The pilot in command is responsible for complying with all items
in the Pilot Operating Handbook and applicable STCs.
I certify this checklist has been reviewed for accuracy.
________________________1/1/06__
Director of Maintenance Date

Checklists Notes

ABOUT CHECKLISTS
Standard operating practices in aviation have advanced somewhat since the first Cessna was sold commercially. So much so that the latest Cessna's are equipped with glass cockpits! It is a great tribute to Clyde Cessna that we are still flying the early models in General Aviation today, however the procedures issued with the aircraft are no longer enough for the complex environment and in striving towards the ultimate aviation goal of zero accident rate.
Standard accepted practices now define the use and application of checklists for normal, abnormal, and emergency operations. This introduction attempts to explain these concepts to those not familiar with checklist operation in the attempt to prevent misuse.
A checklist is used to confirm completion of vital actions, AFTER completion of all required actions, on each critical stage of the flight. As such checklists attempt to include critical items only, especially where inflight operation is concerned. Acronyms and flow patterns provide useful memory aids for completion of the required actions prior to reading the checklist, and for this purpose generic acronyms and standard flow patterns are highly recommended on light aircraft, especially if operating on more than one type.
A checklist, however, should not be generic, and needs to be modified for your aircraft type and serial number, which is why this document is free. If you wish to obtain a personalised checklist for your aircraft, see more details below.
When reading a normal checklist, the item should be read, followed by a glance at the item (eyes normally but follow through with touch is ok), and the required response. To keep track of where you are on the checklist normally the checklist is read with thumbs on each side of the item being checked, or one thumb next to the item being checked. Single column checklists are normally easier for this, but we found the A5 format easiest for reference in a single pilot environment. Users can choose customise layout to suit their own purposes.
In the early days of checklist use, they were often used incorrectly as 'do-lists'. Do-lists are where a pilot read the item, then completed the action required and read the response. Do-lists should normally only be used for emergencies and abnormal operations. A Do-list contains BOLD items, or boxed items, which must be memorised. The philosophy of BOLD memory recall items has only been introduced in Cessna aircraft in the 1980s. Checklists from manuals produced prior to this, and updated, have been included BOLD items based on common sense application of later models requirements. Early flight manuals complicate this concept by listing 'DO-lists' only in the normal operating procedures. The easy way to see if this is the case, is by the appearance of items such as 'Starter................ENGAGE'.
This is clearly not an item that needs to be checked but an action that should be accomplished, and this makes the process rather confusing. Common sense application of later checklists and standad practises must be used in this case.

CHECKLISTS IN A SINGLE CREW OPERATION
It may not always be practical to read a checklist in flight for a single pilot aircraft. If checklists are used in flight, it is recommended that a 'control column' type checklist is used, whereupon the critical in flight checks are attached (either permanently with glue or temporarily with press-stick for example) to the control column or similar location where they can be read easily without distraction from flying duties. A velcro dot can be used if the whole checklist is to be placed in a relevant position, so that you can position the checklist in the desired position for takeoff and landing and stow the checklist at other times.

COPYRIGHT
This document is available in open office format at www.redskyventures.org, or by emailing the author,
in the interests of the principle of
“shared resources = improved aviation safety”.
There is no copyright claimed on this document in an unmodified state, provided it is distributed free or without profit.
Pilots, operators, flight schools and anyone else involved in aviation may download the soft document and modify as desired. Once you have placed your own speeds, logos, and registrations on it, please remove our copyright, and use however you need.
Credit for original version and links to our site are appreciated.

MODIFICATION
to modify this document to make it useable in an aircraft:
(open office version)
- Remove the unwanted pages
- Review and audit all the speeds and checklists according to the aircraft's POH;
- ensure all operating supplements and additional equipment are included;
- review the checklist for any local or operator differences (frequences, cold/hot weather, high altitudes, ATC);
- Change the model type, year and include the serial number on each page
- Change the aircraft registration and type in the footer, include the operator if required;
- Include the operating note on the last page with a signature from the responsible person in your organisation, as required;
- Print, lamin adsxt eds da nddxc dxc
- Where required submit the checklist to t he civil aviation authority with your POH for approval

SERVICES
If you require help with your checklist customisation, email the author, this service is available by providing your aircraft type and serial number, a scanned copy of the POH, and a photograph of the aircraft operating panels.

DISCLAIMER
The checklists provided in this document are based on standard international training practices. And they have been compiled from the information contained in the C210 Pilot's Operating Handbooks.
These checklists must be used by an appropriately licensed pilot, and may not be used in any manner that contradicts the manufacturers Pilot's Operating Handbook. Content of the checklist must be checked for compliance with your aircraft's serial number specific Manufacturer's Pilot's Operating Handbook.

The author accepts no liability for incorrect use of these checklists.

CONTACT THE AUTHOR:

Contact the author on
email: redskyventures@gmail.com
PO Box 11288 Windhoek
Ph +264 081 244 6336
or +971 50 563 7448

This checklist is a guide to coordinate Pilot Operating Handbook
and STC data applicable to this particular aircraft only.
The applicable Pilot Operating Handbook and STC installations
 Remain the official documentation for this aircraft.
The pilot in command is responsible for complying with all items
in the Pilot Operating Handbook and applicable STCs.
I certify this checklist has been reviewed for accuracy.

______________________
Signature Responsible Person
________________________
Title
_____________
Date (dd-mmm-yy)

CESSNA
NORMAL CHECKLIST

Pre Start
Tach/Hobbs/Time	RECORDED
Passenger Briefing	COMPLETE
Preflight Inspection	COMPLETE
Seats / Seatbelts	ADJUST, LOCK
Brakes...	SET/HOLD
Cowl Flaps	OPEN
Avionics	OFF
Electrical Equipment	OFF
Landing Gear	DOWN
Fuel Selector Valve	FULLER TANK
Mixture....	RICH
Propeller..	HIGH RPM
Rotating Beacon....	ON
-----------MASTER ON, READY TO START-----------
Landing Gear Horn	PRESS TO TEST
Circuit Breakers	CHECK IN
Prime.....	.AS REQ’D
Throttle......	½ CENTIMETER
Prop Area.......	CLEAR

After Start
Oil Pressure	GREEN
Mixture....	SET FOR TAXI
Engine Instruments....	CHECK
Taxi, Nav. Lights	AS REQUIRED
Flaps......	RETRACTED
Transponder...	STANDBY

Taxi
Brakes...	RELEASE, CHECK
Alternate Tank	CHECKED
Flight Instruments	TEST AND CHECK
Nav instruments ....	TEST

Pre-Run Up
Parking Brake	SET
Cabin Doors/Windows	CLOSED/LOCKED
Cowls	OPEN
Fuel Selector	FULLER TANK
Mixture	SET
Engine Instruments	GREEN

C210N 1979

NORMAL CHECKLIST

Pre Takeoff
Flight Controls	FREE AND CORRECT
Trims .......	SET FOR TAKEOFF
Mixture..	CHECKED, SET FOR TAKEOFF
Power.......	1700RPM CHECKED
Engine Instruments...CHECKED AT 1700rpm
Magnetos	CHECKED
Propeller Governor	CYCLED
Ammeter	CHECKED UNDER LOAD
Suction Gauge....	CHECKED
DI .........	SET TO COMPASS
Throttle friction lock	SET
Idle	CHECKED
Magnetos ...	BOTH
Propeller Pitch	FULL FINE
Fuel	CORRECT TANK, QTY CHECKED
Flaps......	SET FOR TAKEOFF
Radios....	SET FOR DEPARTURE
Navigation / GPS	SET FOR DEPARTURE
Flight Instruments....	CHECKED AND SET
Seats and Seatbelts..	SECURE
Electrics...	CB's CHECKED
Emergency & Dep. Brief	COMPLETED
Takeoff Power Setting/Fuel Flow	NOTED
Park Brake	RELEASED

Line Up
(REmember What To Do Last)
Runway Area.......	CLEAR
Engine Parameters	GREEN
Wind.......	CHECK
Transponder	SET TO ALTITUDE
DI...........	ALIGNED WITH COMPASS	CORRECT RWY HEADING
Landing light, strobes	ON

After Takeoff (above 1000' AGL)
Brakes....	CHECK
Undercarriage	UP, ORANGE LIGHT
Power/Pitch	SET
Mixture...	ADJUST
Fuel	CHECKED
Flaps	UP
Engine Parameters	GREEN
Lights....	AS REQUIRED

NORMAL CHECKLIST

Cruise
Power/Prop	SET
Elevator/Rudder trim	ADJUST
Mixture....	LEAN FOR ALTITUDE
Cowl Flaps	CLOSED/AS REQ’D

Descent
Fuel	CORRECT TANK, QTY CHECKED
Radios	SET
Engine Instruments	CHECKED
DI	ALIGNED
Approach Briefing	COMPLETE
Altimeter	SET
Mixture....	SET
Cowl Flaps	CLOSED
Lights.....	ON/AS REQ'D

Downwind
Seats / Seatbelts	CHECK SECURE
Fuel	FULLER TANK
Brakes....	CHECK
Landing Gear	DOWN, GREEN LIGHT
Mixture...	SET

Final
Cowl Flaps	OPEN
Mixture	SET FOR GO ROUND
Landing Gear	DOWN, ONE GREEN LIGHT
Propeller Pitch	FULL FINE

After Landing
Cowl Flaps	OPEN
Wing Flaps.....	RETRACT
Land, Strobe lights	OFF
Transponder	STANDBY

Shutdown and Securing
Power.....	IDLE
Avionics and Electrics	OFF
Mixture.......	IDLE CUTOFF
Magnetos......	OFF
Master....	OFF
Control Lock	INSTALLED
Tach/Hobbs/Time	RECORDED

C210N 1979

REFERENCE INFORMATION

Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW, Sea Level , ISA conditions.
VT/O 50ft- Flap 10 (max perf.)	69 KIAS
VX – Best Angle of Climb	80 KIAS
VY – Best Rate of Climb	Vysl 96 KIAS
VY – Best Rate of Climb	Vy10,000ft89 KIAS
Vref – Minimum Approach Speed	72 KIAS
VA – Maneuvering Speed	125-101 KIAS
Maximum demonstrated crosswind	21kts
PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	165 KIAS
VNE – Red Line (Never Exceed)	200 KIAS
VS – Stall Clean	69 KIAS
VSO – Stall landing configuration	57 KIAS
VFE – Max. Flap Extn 0-30º	115 KIAS
VFE – Max. Flap Extn 0-10 º	150 KIAS
VLo – Max. Gear Extension	165 KIAS
VLR – Min. Flap Retraction	80 KIAS
EMERGENCY OPERATION
Best glide Speed	75-85 KIAS
Precautionary Landing:
-Slow Safe Cruise	90-110 KIAS
-Approach (flap up)	85 KIAS
-Approach (flap full)	75 KIAS
Ditching (full flap)	75 KIAS
Engine failure after takeoff (flap up)	85 KIAS
Engine failure A.T.O(flap down)	80 KIAS
Engine Failure in flight	85 KIAS
Landing without power (flap up)	90 KIAS
Landing without power (flap down)	80 KIAS
Operating performance
Planning	65lt/hr
Plan Cruise speed	145KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
All Africa TIBA	126.9
Uncontrolled/Unmanned:	124.8
Training Areas:	124.4
EMERGENCY PROCEDURES
Engine Failure
TAKEOFF
NOTE: Bold Items are immediate recall Items, other times may be followed up by the use of the AFM checklist.
Throttle	IDLE
Brakes	APPLY
Flaps	UP
Mixture	CUTOFF
Ignition	OFF
Master switch	OFF
AFTER TAKEOFF
Airspeed	85KIAS
Mixture	CUTOFF
Fuel Selector Valve	OFF
Ignition	OFF
Gear	AS REQUIRED
Flaps	AS REQUIRED
Master switch	OFF
DURING FLIGHT
IMMEDIATE ACTIONS
Airspeed	85KIAS
Field	SELECT
Approach	PLAN

FAULT FINDIND/RESTART
Fuel Quantity	CHECK
Fuel Selector Valve	ON FULLER TANK
Mixture	RICH
Fuel Pump	ON 3-5 SECONDS
Ignition	BOTH
(or START if not windmilling)
Throttle	ADVANCE
If no start obtained proceed with Forced Landing Procedure
COMMUNICATE
Mayday	Transmit Active or 121.5
Transponder	7700
Passengers	BRIEF

SECURE
Mixture	CUTOFF
Fuel SelectoR	OFF
Ignition	OFF

C210N 1979

FINAL
Airspeed	90KIAS (flap up)
80KIAS (flap down)
Gear	AS REQUIRED
Flaps	AS REQUIRED
Master switch	OFF
Doors	UNLATCH
Touchdown	TAIL LOW

Engine Fire
During Start
Starter	CRANK
To draw away flames, If Engine Starts:
Power	1700RPM
For a few minutes until flames appear to be extinguished, or if engine does not start:
Mixture	CUT-OFF
Ignition	OFF
Master	OFF
Inspect damage
During Flight
Mixture	CUT-OFF
Fuel	OFF
Master	OFF
Cabin Heat and Air	OFF
Airspeed	140MPH/120KIAS
If fire is not extinguished Increase Speed and/or Sideslip as required to obtain an incombustible mixture.
Proceed with Engine Failure in Flight Actions
Cabin Fire
On the Ground
Master Switch	OFF
Cabin Vents/Air/Heat	CLOSED
Fire Extinguisher	ACTIVATE
Cabin Vents/Windows	OPEN

During flight
Follow Above Procedure, Once Fire is extinguished:
Electrics/Avionics	OFF
Master	ON
Avionics/Electrics	On, one at a time
Land at the nearest Suitable Airfield

Electrical Fire
Unknown Source
Master Switch	OFF
All Avionics and Electrics	OFF
Circuit Breakers	PULL
If Smoke Ceases:
Cabin	VENTILATE
Master Switch	ON
Essential Electrical/Avionics ON, ONE at a time to isolate cause.
Known Source
Faulty Equipment	OFF
Cabin	Ventilate
Reassess continued flight functionality without faulty equipment.

Spin Recovery
Ailerons	NEUTRAL
Throttle	IDLE
Confirm direction:
RUDDER	FULL OPPOSITE
Elevator	FORWARD TO BREAK STALL
When Spinning Stops:
Rudder	NEUTRALISE
Pitch	EASE OUT OF DIVE

Main Fuel Pump Failure
After Takeoff
Fuel Pump	HI
Hold Fuel Pump in High Position until reaching a safe altitude and power can be reduced to cruise.
Fuel Pump	ON
During Cruise
Mixture	RICH
Fuel Pump	HI
Select HI to restore fuel flow, once fuel flow is restored
Fuel Pump	ON
HI may be needed momentarily for situations with excessive fuel demand.

C210N 1979

Electrical Failure/Overload
Load	REDUCE TO MINIMUM
Alternator	OFF
Alternator CB	TRIP&RESET
Alternator	ON
Load/Power	OK?
If Not:
Master	OFF
Master	ON
IF LOAD still not does not return to normal: PLAN To land at nearest suitable airfield,
Conserve Battery as much as possible,
All non essential electrics off, if necessary Inform ATC and turn master off until approaching circuit. Be prepared for implications of electrical failures on systems(flaps/gear/avionics).

Engine Roughness
Magnetos	CHECK
Mixture	ADJUST
Temperatures/Pressures	CHECK
If roughness continues, plan to land at nearest suitable airfield.

Ditching
Follow forced landing procedure with the following differences:
Heavy Objects from baggage	JETTISON
Gear	UP
Flaps	30
With Power:
Approach	300ft/min ROD, 75KIAS
Land-High Winds	INTO WIND
        -Light winds	PARALLEL TO SWELL
If no power approach at 85KIAS flap up, or 80KIAS flap 10.
Cabin Doors	UNLATCH
Face	CUSHION FOR IMPACT
Aircraft	EVACUATE
Inadvertent Icing Encounter
Pitot heat	ON
Icing conditions	VACATE
turn back or change level to avoid icing.

Refer to POH Emergencies
for full procedure
CESSNA
NORMAL CHECKLIST

Pre Start
Tach/Hobbs/Time	RECORDED
Passenger Briefing	COMPLETE
Preflight Inspection	COMPLETE
Seats / Seatbelts	ADJUST, LOCK
Brakes...	SET/HOLD
Cowl Flaps	OPEN
Avionics	OFF
Electrical Equipment	OFF
Landing Gear	DOWN
Fuel Selector Valve	FULLER TANK
Mixture....	RICH
Propeller..	HIGH RPM
Rotating Beacon....	ON
-----------MASTER ON, READY TO START-----------
Landing Gear Horn	PRESS TO TEST
Circuit Breakers	CHECK IN
Prime.....	50-60lbs/AS REQ’D
Throttle......	½ CENTIMETER
Prop Area.......	CLEAR
After Start
Oil Pressure	GREEN
Mixture....	SET FOR TAXI
Engine Instruments....	CHECK
Taxi, Nav. Lights	AS REQUIRED
Flaps......	RETRACTED
Transponder...	STANDBY
Taxi
Brakes...	RELEASE, CHECK
Alternate Tank	CHECKED
Flight Instruments	TEST AND CHECK
Nav instruments ....	TEST
Pre-Run Up
Parking Brake	SET
Cabin Doors/Windows	CLOSED/LOCKED
Cowls	OPEN
Fuel Selector	FULLER TANK
Mixture	SET
Engine Instruments	GREEN

C210L 1973

NORMAL CHECKLIST

Pre Takeoff
Flight Controls	FREE AND CORRECT
Trims .......	SET FOR TAKEOFF
Mixture..	CHECKED, SET FOR TAKEOFF
Power.......	1700RPM CHECKED
Engine Instruments...CHECKED AT 1700rpm
Magnetos	CHECKED
Propeller Governor	CYCLED
Ammeter	CHECKED UNDER LOAD
Suction Gauge....	CHECKED
DI .........	SET TO COMPASS
Throttle friction lock	SET
Idle	CHECKED
Magnetos ...	BOTH
Propeller Pitch	FULL FINE
Fuel	CORRECT TANK, QTY CHECKED
Flaps......	SET FOR TAKEOFF
Radios....	SET FOR DEPARTURE
Navigation / GPS	SET FOR DEPARTURE
Flight Instruments....	CHECKED AND SET
Seats and Seatbelts..	SECURE
Electrics...	CB's CHECKED
Emergency & Dep. Brief	COMPLETED
Takeoff Power Setting/Fuel Flow	NOTED
Park Brake	RELEASED
Line Up
(REmember What To Do Last)
Runway Area.......	CLEAR
Engine Parameters	GREEN
Wind.......	CHECK
Transponder	SET TO ALTITUDE
DI...........	ALIGNED WITH COMPASS, RWY
Landing light, strobes	ON
After Takeoff (above 1000' AGL)
Brakes....	CHECK
Undercarriage	UP, ORANGE LIGHT
Power/Pitch	SET
Mixture...	ADJUST
Fuel	CHECKED
Flaps	UP
Engine Parameters	GREEN
Lights....	AS REQUIRED

NORMAL CHECKLIST

Cruise
Power/Prop	SET
Elevator/Rudder trim	ADJUST
Mixture....	LEAN FOR ALTITUDE
Cowl Flaps	CLOSED/AS REQ’D
Descent
Fuel	CORRECT TANK, QTY CHECKED
Radios	SET
Engine Instruments	CHECKED
DI	ALIGNED
Approach Briefing	COMPLETE
Altimeter	SET
Mixture....	SET
Cowl Flaps	CLOSED
Lights.....	ON/AS REQ'D
Downwind
Seats / Seatbelts	CHECK SECURE
Fuel	FULLER TANK
Brakes....	CHECK
Landing Gear	DOWN, GREEN LIGHT
Mixture...	SET
Final
Cowl Flaps	OPEN
Mixture	SET FOR GO ROUND
Landing Gear	DOWN, ONE GREEN LIGHT
Propeller Pitch	FULL FINE

After Landing
Cowl Flaps	OPEN
Wing Flaps.....	RETRACT
Land, Strobe lights	OFF
Transponder	STANDBY
Shutdown and Securing
Power.....	IDLE
Avionics and Electrics	OFF
Mixture.......	IDLE CUTOFF
Magnetos......	OFF
Master....	OFF
Control Lock	INSTALLED
Tach/Hobbs/Time	RECORDED

C210L 1973

REFERENCE INFORMATION

Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW, Sea Level , ISA conditions.
VR (nml)	70-80 mph
VT/O 50ft	82mph
VX – Best Angle of Climb	Vxsl 85 mph
Vx10,000ft 90 mph
VY – Best Rate of Climb	Vysl 109 mph
Vy10,000ft102 mph
Normal approach (Flap 30)	85-95mph
Vref	82 mph
VA – Maneuvering Speed	115-135 mph

PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	190 mph
VNE – Red Line (Never Exceed)	225 mph
VS – Stall Clean	75 mph
VSO – Stall landing configuration	65 mph
VFE – Max. Flap Extn 0-30º	120 mph
VFE – Max. Flap Extn 0-10 º	160 mph
VLE – Max. Gear Extension	160 mph
VLR – Min. Gear and Flap Retraction	90 mph
EMERGENCY OPERATION
Best glide Speed	85-95 KIAS
Precautionary	90-110 mph
  Field Inspection	10º flap, 100 mph
  Approach (flaps full)	85-95 mph
Engine failure after takeoff	100 mph
Engine Failure in flight flap up	100 mph
Engine Failure in flight flap down	90 mph
Operating performance
Planning	65lt/hr
Plan Cruise speed	145KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
All Africa TIBA	126.9
Uncontrolled/Unmanned:	124.8
Training Areas:	124.4
EMERGENCY PROCEDURES
Engine Failure
TAKEOFF
NOTE: Bold Items are immediate recall Items, other times may be followed up by the use of the AFM checklist.
Throttle	IDLE
Brakes	APPLY
Flaps	UP
Mixture	CUT-OFF
Ignition	OFF
Master switch	OFF
AFTER TAKEOFF
Airspeed	100 MPH/85KIAS
Mixture	CUT-OFF
Fuel Selector Valve	OFF
Ignition	OFF
Gear	AS REQUIRED
Flaps	AS REQUIRED
Master switch	OFF
DURING FLIGHT
IMMEDIATE ACTIONS
Airspeed	100MPH/85KIAS(Flaps UP)
90MPH/80KIAS (Flaps DOWN)
Field	SELECT
Approach	PLAN

FAULT FINDIND/RESTART
Fuel Quantity	Check
Fuel Selector Valve	ON FULLER TANK
Mixture	RICH
Fuel Pump	ON 3-5 Seconds
Ignition	BOTH
(or START if not windmilling)
Throttle	Advance
If no start obtained proceed with Forced Landing Procedure

COMMUNICATE
Mayday	Transmit Active or 121.5
Transponder	7700
Passengers	BRIEF

SECURE
Mixture	CUTOFF
Fuel Selector	OFF
Ignition	OFF

FINAL
Gear	As Required
Flaps	As Required
Master switch	Off
Doors	UNLATCH
Touchdown	TAIL LOW

Engine Fire
During Start
Starter	CRANK
To draw away flames, If Engine Starts:
Power	1700rpm
For a few minutes until flames appear to be extinguished, or if engine does not start:
Mixture	CUTOFF
Ignition	OFF
Master	OFF
Inspect damage
During Flight
Mixture	CUTOFF
Fuel	OFF
Master	OFF
Cabin Heat and Air	OFF
Airspeed	140MPH/120KIAS
If fire is not extinguished Increase Speed and/or Sideslip as required to obtain an incombustible mixture. Proceed with Engine Failure in Flight Actions
Cabin Fire
On the Ground
Master Switch	OFF
Cabin Vents/Air/Heat	CLOSED
Fire Extinguisher	ACTIVATE
Cabin Vents/Windows	OPEN

During Flight
Follow Above Procedure, Once Fire is extinguished:
Electrics/Avionics	OFF
Master	ON
Avionics/Electrics	On, one at a time
Land at the nearest Suitable Airfield

C210L 1973

Electrical Fire
Unknown Source
Master Switch	OFF
All Avionics and Electrics	OFF
Circuit Breakers	PULL
If Smoke Ceases:
Cabin	VENTILATE
Master Switch	ON
Essential Electrical/Avionics ON, ONE at a time to isolate cause.
Known Source
Faulty Equipment	OFF
Cabin	Ventilate
Reassess continued flight functionality without faulty equipment.

Spin Recovery
Ailerons	NEUTRAL
Throttle	IDLE
Confirm direction
RUDDER	FULL OPPOSITE
Elevator	FORWARD TO BREAK STALL
Rudder	Neutralise when spinning stops
Pitch	EASE OUT OF DIVE

Main Fuel Pump Failure
After Takeoff
Fuel Pump	HI
Hold Fuel Pump in High Position until reaching a safe altitude and power can be reduced to cruise.
Fuel Pump	ON
During Cruise
Mixture	RICH
Fuel Pump	HI
Select HI to restore fuel flow, once fuel flow is restored
Fuel Pump	ON
HI may be needed momentarily for situations with excessive fuel demand.

Electrical Failure/Overload
Load	VERIFY
REDUCE TO MINIMUM
Alternator	OFF
Alternator CB	TRIP&RESET
Alternator	ON
Load/Power	OK?
If Not:
Master	OFF
Master	ON
IF LOAD still not does not return to normal: PLAN To land at nearest suitable airfield,
Conserve Battery as much as possible,
All non essential electrics off, if necessary Inform ATC and turn master off until approaching circuit. Be prepared for implications of electrical failures on systems(flaps/gear/avionics).

Engine Roughness
Magnetos	CHECK
Mixture	ADJUST
Temperatures/Pressures	CHECK
If roughness continues, plan to land at nearest suitable airfield.

C210L 1973

NORMAL CHECKLIST

Pre Start
Tach/Hobbs/Time	RECORDED
Passenger Briefing	COMPLETE
Preflight Inspection	COMPLETE
Seats / Seatbelts	ADJUST, LOCK
Brakes...	SET/HOLD
Cowl Flaps	OPEN
Avionics	OFF
Electrical Equipment	OFF
Landing Gear	DOWN
Fuel Selector Valve	FULLER TANK
Mixture....	RICH
Propeller..	HIGH RPM
Rotating Beacon....	ON
-----------MASTER ON, READY TO START-----------
Landing Gear Horn	PRESS TO TEST
Circuit Breakers	CHECK IN
Prime.....	50-60lbs/AS REQ’D
Throttle......	½ CENTIMETER
Prop Area.......	CLEAR
After Start
Oil Pressure	GREEN
Mixture....	SET FOR TAXI
Engine Instruments....	CHECK
Taxi, Nav. Lights	AS REQUIRED
Flaps......	RETRACTED
Transponder...	STANDBY
Taxi
Brakes...	RELEASE, CHECK
Alternate Tank	CHECKED
Flight Instruments	TEST AND CHECK
Nav instruments ....	TEST
Pre-Run Up
Parking Brake	SET
Cabin Doors/Windows	CLOSED/LOCKED
Cowls	OPEN
Fuel Selector	FULLER TANK
Mixture	SET
Engine Instruments	GREEN

C210L 1974

NORMAL CHECKLIST

Pre Takeoff
Flight Controls	FREE AND CORRECT
Trims .......	SET FOR TAKEOFF
Mixture..	CHECKED, SET FOR TAKEOFF
Power.......	1700RPM CHECKED
Engine Instruments...CHECKED AT 1700rpm
Magnetos	CHECKED
Propeller Governor	CYCLED
Ammeter	CHECKED UNDER LOAD
Suction Gauge....	CHECKED
DI .........	SET TO COMPASS
Throttle friction lock	SET
Idle	CHECKED
Magnetos ...	BOTH
Propeller Pitch	FULL FINE
Fuel	CORRECT TANK, QTY CHECKED
Flaps......	SET FOR TAKEOFF
Radios....	SET FOR DEPARTURE
Navigation / GPS	SET FOR DEPARTURE
Flight Instruments....	CHECKED AND SET
Seats and Seatbelts..	SECURE
Electrics...	CB's CHECKED
Emergency & Dep. brief	COMPLETED
Takeoff Power Setting/Fuel Flow	NOTED
Park Brake	RELEASED
Line Up
(REmember What To Do Last)
Runway Area.......	CLEAR
Engine Parameters	GREEN
Wind.......	CHECK
Transponder	SET TO ALTITUDE
DI...........	ALIGNED WITH COMPASS, RWY
Landing light, strobes	ON
After Takeoff (above 1000' AGL)
Brakes....	CHECK
Undercarriage	UP, ORANGE LIGHT
Power/Pitch	SET
Mixture...	ADJUST
Fuel	CHECKED
Flaps	UP
Engine Parameters	GREEN
Lights....	AS REQUIRED

NORMAL CHECKLIST

Cruise
Power/Prop	SET
Elevator/Rudder trim	ADJUST
Mixture....	LEAN FOR ALTITUDE
Cowl Flaps	CLOSED/AS REQ’D
Descent
Fuel	CORRECT TANK, QTY CHECKED
Radios	SET
Engine Instruments	CHECKED
DI	ALIGNED
Approach Briefing	COMPLETE
Altimeter	SET
Mixture....	SET
Cowl Flaps	CLOSED
Lights.....	ON/AS REQ'D
Downwind
Seats / Seatbelts	CHECK SECURE
Fuel	FULLER TANK
Brakes....	CHECK
Landing Gear	DOWN, GREEN LIGHT
Mixture...	SET
Final
Cowl Flaps	OPEN
Mixture	SET FOR GO ROUND
Landing Gear	DOWN, ONE GREEN LIGHT
Propeller Pitch	FULL FINE

After Landing
Cowl Flaps	OPEN
Wing Flaps.....	RETRACT
Land, Strobe lights	OFF
Transponder	STANDBY
Shutdown and Securing
Power.....	IDLE
Avionics and Electrics	OFF
Mixture.......	IDLE CUTOFF
Magnetos......	OFF
Master....	OFF
Control Lock	INSTALLED
Tach/Hobbs/Time	RECORDED

C210L 1974

REFERENCE INFORMATION
Note: ASI in mph, POH in KIAS both speeds included where important
Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW, Sea Level , ISA conditions.
VR (nml)	65-70KIAS/70-80 mph
VT/O 50ft	72KIAS/83mph
VX – Best Angle of Climb Vxsl 75KIAS/87mph
Vx10,000ft 80KIAS/92mph
VY – Best Rate of Climb	Vysl 97KIAS/111 mph
Vy10,000ft92KIAS/106 mph
Normal approach (Flap 30)	75-85KIAS
Vref	71 KIAS/82 mph
VA – Maneuvering Speed	96-119KIAS
PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	168KIAS
VNE – Red Line (Never Exceed)	199KIAS
VS – Stall Clean	68KIAS/79 mph
VSO – Stall landing	55KIAS/64 mph
VFE – Max. Flap Extn 0-30º	105KIAS120 mph
VFE – Max. Flap Extn 0-10 º140KIAS160 mph
VLE – Max. Gear Extension	140KIAS160 mph
VLR – Min. Gear/Flap Retrn	80KIAS/90mph
EMERGENCY OPERATION
Best glide Speed	75-85 KIAS/85-95mph
Precautionary	75-85 KIAS
  Field Inspection	10º flap, 85KIAS/100 mph
  Approach (flaps full)	75KIAS/90 mph
Engine failure after takeoff	85KIAS/100 mph
Engine Failure flap up	90KIAS/105 mph
Engine Failure flap down	80KIAS/95 mph
Operating performance
Planning	65lt/hr
Plan Cruise speed	145KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
All Africa TIBA	126.9
Uncontrolled/Unmanned:	124.8
Training Areas	124.4

EMERGENCY PROCEDURES
Engine Failure
TAKEOFF
NOTE: Bold Items are immediate recall Items, other times may be followed up by the use of the AFM checklist.
Throttle	IDLE
Brakes	APPLY
Flaps	UP
Mixture	CUT-OFF
Ignition	OFF
Master switch	OFF
AFTER TAKEOFF
Airspeed	100 MPH/85KIAS
Mixture	CUT-OFF
Fuel Selector Valve	OFF
Ignition	OFF
Gear	AS REQUIRED
Flaps	AS REQUIRED
Master switch	OFF
DURING FLIGHT
IMMEDIATE ACTIONS
Airspeed	100MPH/85KIAS(Flaps UP)
90MPH/80KIAS (Flaps DOWN)
Field	SELECT
Approach	PLAN

FAULT FINDIND/RESTART
Fuel Quantity	Check
Fuel Selector Valve	ON FULLER TANK
Mixture	RICH
Fuel Pump	ON 3-5 Seconds
Ignition	BOTH
(or START if not windmilling)
Throttle	Advance
If no start obtained proceed with Forced Landing Procedure

COMMUNICATE
Mayday	Transmit Active or 121.5
Transponder	7700
Passengers	BRIEF

SECURE
Mixture	CUTOFF
Fuel Selector	OFF
Ignition	OFF

FINAL
Gear	As Required
Flaps	As Required
Master switch	Off
Doors	UNLATCH
Touchdown	TAIL LOW

Engine Fire
During Start
Starter	CRANK
To draw away flames, If Engine Starts:
Power	1700rpm
For a few minutes until flames appear to be extinguished, or if engine does not start:
Mixture	CUTOFF
Ignition	OFF
Master	OFF
Inspect damage

During Flight
Mixture	CUTOFF
Fuel	OFF
Master	OFF
Cabin Heat and Air	OFF
Airspeed	140MPH/120KIAS
If fire is not extinguished Increase Speed and/or Sideslip as required to obtain an incombustible mixture. Proceed with Engine Failure in Flight Actions

Cabin Fire
On the Ground
Master Switch	OFF
Cabin Vents/Air/Heat	CLOSED
Fire Extinguisher	ACTIVATE
Cabin Vents/Windows	OPEN

During Flight
Follow Above Procedure, Once Fire is extinguished:
Electrics/Avionics	OFF
Master	ON
Avionics/Electrics	On, one at a time
Land at the nearest Suitable Airfield

C210L 1974
Electrical Fire
Unknown Source
Master Switch	OFF
All Avionics and Electrics	OFF
Circuit Breakers	PULL
If Smoke Ceases:
Cabin	VENTILATE
Master Switch	ON
Essential Electrical/Avionics ON, ONE at a time to isolate cause.
Known Source
Faulty Equipment	OFF
Cabin	Ventilate
Reassess continued flight functionality without faulty equipment.

Spin Recovery
Ailerons	NEUTRAL
Throttle	IDLE
Confirm direction
RUDDER	FULL OPPOSITE
Elevator	FORWARD TO BREAK STALL
Rudder	Neutralise when spinning stops
Pitch	EASE OUT OF DIVE

Main Fuel Pump Failure
After Takeoff
Fuel Pump	HI
Hold Fuel Pump in High Position until reaching a safe altitude and power can be reduced to cruise.
Fuel Pump	ON
During Cruise
Mixture	RICH
Fuel Pump	HI
Select HI to restore fuel flow, once fuel flow is restored
Fuel Pump	ON
HI may be needed momentarily for situations with excessive fuel demand.

Electrical Failure/Overload
Load	VERIFY
REDUCE TO MINIMUM
Alternator	OFF
Alternator CB	TRIP&RESET
Alternator	ON
Load/Power	OK?
If Not:
Master	OFF
Master	ON
IF LOAD still not does not return to normal: PLAN To land at nearest suitable airfield,
Conserve Battery as much as possible,
All non essential electrics off, if necessary Inform ATC and turn master off until approaching circuit. Be prepared for implications of electrical failures on systems(flaps/gear/avionics).

Engine Roughness
Magnetos	CHECK
Mixture	ADJUST
Temperatures/Pressures	CHECK
If roughness continues, plan to land at nearest suitable airfield.

C210L 1974